MATERIAL SAFETY DATA SHEET

| INTERLUBE CORPORATION 4646 Baker Avenue Cincinnati, Ohio 45212 | Phone: (513) 531-1777 Fax: (513) 531-0193 Emergency Telephone: 800-424-9300 Chemtrec |
| --- | --- |
| SECTION I: IDENTIFICATION INFORMATION |
| Product Trade Name: | Degreaser FG (Aerosol) | Revision Date: | August 24, 2009 |
| Chemical Name & Synonyms: | Not Applicable |
| Chemical Family: | Not Applicable |
|  | Health | Fire | Reactivity |
| NFPA Code: | 1 | 2 | 0 |
| SECTION II: HAZARDOUS INGREDIENTS |
| Ingredient | CAS# | Appx% | TLV (Units) |
| Heavy Hydrotreated Naphtha | 84742-48-9 |  | None Estab. |
| Carbon Dioxide (propellant) | 124-38-9 |  | 10,000 ppm |
| Contains no SARA III Section 313 chemicals at reportable levels. |  |  |  |
| SECTION III: PHYSICAL DATA |
| Boiling Point ((F): | ND ( Conc. >375ºF ) | Specific Gravity: | 0.77 |
| Vapor Pressure (mm Hg): | ND ( in can 90 psig@70ºF ) | % Volatile by Vol: | 100 |
| Vapor Density (Air = 1): | >5 | Solubility in Water: | Nil |
| Evaporation Rate (Bu.Ac. =1): | <1 |
| Appearance and Odor: | Water White Colored Liquid, Nearless Odorless |
| SECTION IV: FIRE AND EXPLOSION HAZARD DATA |
| Flash Point (Method): | Flammable Spray by USA Aerosol Flame Projection Test. | Flammable Limits ((F) |
| Extinguishing Media: | Water Fog, CO2, Dry Chemicals, Foam | Lower: | ND | Upper: | ND |
| Special Fire Fighting Procedures: | Treat as oil fire. Keep cans cool to prevent rupture. |
| Unusual Fire and Explosion Hazards: | Aerosol cans may explode if severely overheated. |

| Product: Degreaser FG (Aerosol) | Revision Date: August 24, 2009 |
| --- | --- |
| SECTION V: HEALTH HAZARD DATA |
| Threshold Limit Value: | None Established. |
| Effects of Overexposure: | Liquid is practically non irritating to the eyes and slightly irritating to the skin. High concentrations may result in central nervous system depression. Vapors may be irritating. Ingestion may be harmful |
| or fatal – severe aspiration hazard – chemical pneumonitis. |
| Emergency and First Aid Procedures: | EYE CONTACT: Flush thoroughly with water for 15 minutes and get medical attention. |
| OVER INHALATION: Remove to fresh air if effects occur. |
| SKIN CONTACT: Wash with soap and water. |
| INGESTION: Get medical attention. Do not induce vomiting. |
| SECTION VI: REACTIVITY DATA |
| Stability: | Stable |
| Incompatibility: | Oxidizers |
| Hazardous Decomposition Products: | COx, & Asphyxiants |
| Hazardous Polymerization: | Will not occur. |
| SECTION VII: SPILL OR LEAK PROCEDURES |
| Steps to be taken in case material is released or spilled: | Contain spill. Absorb on suitable media. Eliminate ignition sources. |
| Waste Disposal: | Dispose of in accordance with Local, State, & Federal regulations. |
| SECTION VIII: SPECIAL PROTECTION INFORMATION |
| Respiratory Protection: | Use NIOSH approved self contained breathing apparatus if required |
| Ventilation: | Not normally required. Use local exhaust if required. |
| Protective Gloves: | Not normally required. |
| Eye Protection: | Recommended. |
| Other PPE: | Not normally required |
| SECTION IX: SPECIAL PRECAUTIONS |
| CAUTION: Spray Flammable. Avoid prolonged or repeated contact with the skin - can cause moderate irritation, defatting. Avoid prolonged or repeated breathing of vapors. Do not ingest - harmful or fatal if swallowed - aspiration into lungs can cause chemical pneumonitis. See Emergency and and First Aid Procedures. |
| SECTION X: TRANSPORTATION AND LABELING |
| DOT Shipping Name: | Consumer Commodity | Packaging Group: | None |
| DOT Hazard Class: | ORM-D | ID Number: | Not Required |
| Labels: | None | RQ: | None |
| The information presented in this material safety data sheet is, to the best of our knowledge and belief, accurate as of the revision date. Any information, data, and opinions herein are based upon information provided and available to us. Interlube Corporation makes no warranty or representation, express or implied, to any person, as to its accuracy, reliability, or completeness. INTERLUBE CORPORATION EXPRESSLY DISCLAIMS ALL WARRANTIES OF EVERY NATURE, INCLUDING WARRANTIES OF MERCHANTIBILITY AND FITNESS FOR A PARTICULAR PURPOSE regarding any information, data, and opinions in this document and the use or suitability of the product described. The information, data, and opinions in this document are offered solely for the user’s consideration, investigation, and verification. Any use of this material safety data sheet and the product described must be in accordance with all local, state, and federal laws and regulations. |